## Slide 1: Magnetic Gear
Ondřej Sedláček
FOR TEAM GCHD
10

## Slide 2: Table of contents
Task definition
Relevant parameters and phenomena
Measuring spinner parameters
Determining drag
Simulation and testing
Driven spinner experiments
  Magnetic coupling
  Theoretical coupling limits
  Torque transfer
Introduction

## Slide 3: Task definition
Take several identical fidget spinners and attach neodymium magnets to their ends. If you place them side by side on a plane and rotate one of them, the remaining ones start to rotate only due to the magnetic field. Investigate and explain the phenomenon.
We focused on the behaviour of 1 or 2 spinners, since anything above that starts behaving chaotically and is hard to quantitatively measure.
We always kept all the spinners in plane and firmly put in place, so that they‘d not move around.
We used identical spinners with identical magnets and magnet amounts.
Introduction

## Slide 4: Relevant parameters
Configuration:
  Relative positions of spinners
  Angular velocities
  Phase offsets
  Attachment direction of the magnets – vertical, eccentric, tangent
Drag – constant, quadratic
Spinner parameters
  Size
  Amount of spinner arms
  Moment of inertia ()
Magnet strength and size
Introduction
Vertical
Eccentric
Tangent
Notes: We chose the vertical orientation, since it held on the easiest.
Other configuration might‘ve improved the torque tranfer, since B interactions are non-zero.

## Slide 5: Relevant phenomena
Magnet – magnet interactions
  We used cube NdFeB magnets (5mm, grade N35)
  We model each magnet as a magnetic dipole
  Force iteraction:
  Torque due to generated magnetic field:
Other forces on the spinner
  Concentric forces on the ball bearing => increasing drag
  Oscillations and rattling of the ball bearings
Introduction
Magnetic dipole moment:
Notes: Magnetic dipole approximation breaks down at small distances (comparable to the size of the magnet)

## Slide 6: Moment of inertia
Calculated from the model of a mathematical pendulum
The spinner was suspended with magnets attached to one arm and left to swing freely
Our result are comparable to results found online:
https://www.wired.com/2017/05/physics-of-a-fidget-spinner/
Measurements

## Slide 7: Remanence
Can be either calculated from the generated magnetic field or from force between the magnets
Simplifying the previous equations for dipole force and magnetic field:
We used both methods:
  the force was measured via a scale (used for a singular magnet)
  the field was measured using a mobile phone magnetometer (with the Earth‘s magnetic field being accounted for)
Measurements

## Slide 8: Remanence - results
We measured for 1, 2 and 3 cube magnet stacks as well as a larger (old) NdFeB magnet
Measurements

## Slide 9: Remanence – more result
Additional information
t [s]
B [T]

## Slide 10: Drag
Our theory suggest, that the main sources of drag would be:
Constant drag from the bearing friction – constant in respect to (denoted )
Turbulent drag on the spinner geometry – quadratic in respect to (denoted )
(Possibly some linear component – linear in respect to (denoted ))
… denotes the total time before the spinner stops
Measurements
 | Without linear component () | With linear component ()
Differential equation |  | 
Solution |  | 
Differential equation |  | 
Solution |  | 

## Slide 11: Drag - results
Measurements

## Slide 12: Drag – more result
Additional information
The large magnet is modeled as a single magnetic dipole at its center