## Slide 1: Magnetic Gear
Ondřej Sedláček
FOR TEAM GCHD
10

## Slide 2: Table of contents
Task definition
Relevant parameters and phenomena
Magnetic coupling
Simulation and testing
Torque transfer
Determining drag
(Measuring spinner parameters)
Summary
Introduction

## Slide 3: Task definition
Take several identical fidget spinners and attach neodymium magnets to their ends. If you place them side by side on a plane and rotate one of them, the remaining ones start to rotate only due to the magnetic field. Investigate and explain the phenomenon.
We focused on the transfer of torque and angular velocity for 2 spinners, since anything above that starts behaving chaotically and is hard to quantitatively measure.
We always kept all the spinners in one plane and firmly put in place, so that they wouldn’t move around.
We used identical spinners with identical magnets and magnet counts.
Introduction
Notes: Focused on torque and angular velocity
We analytically described drag

## Slide 4: Observed behaviour
A quickly rotating spinner acts similarly to a permanent magnet
Two spinners start behaving chaotically at low RPM
Introduction
We also experimented with multiple spinners, but we were unable to come to any conclusions
Notes: We should add some simple examples/videos, so that everyone catches on
Take the spinners with magnets and the spinner with the metal plate with me! Take the magnetic transmission as well!

## Slide 5: More examples
Additional information
We also experimented with spinners, that were not inline => even more chaotic

## Slide 6: Relevant parameters
Configuration:
  Relative positions of spinners
  Angular velocities
  Phase offsets
  Attachment direction of the magnets – vertical, eccentric, tangent
  Attraction / Repulsion
Drag – constant (), quadratic ()
Spinner parameters
  Size
  Amount of spinner arms
  Moment of inertia ()
Magnet strength, size and grade
Introduction
Vertical
Eccentric
Tangent
Notes: We chose the vertical orientation, since it held on the easiest.
Other configuration might‘ve improved the torque tranfer, since B interactions are non-zero.

## Slide 7: Drag – Analytical solution
Our theory suggests, that the main sources of drag would be:
Constant drag from the bearing friction – constant in respect to (denoted )
Turbulent drag on the spinner geometry – quadratic in respect to (denoted )
(Possibly some linear component – linear in respect to (denoted ))
… denotes the total time before the spinner stops
Measurements
 | Without linear component () | With linear component ()
Differential equation |  | 
Solution |  | 
Differential equation |  | 
Solution |  | 
()

## Slide 8: Drag – Comparison of models
Measurements
Notes: Here we compare how well our simulation handles the linear component
The measurements is exceptionally close to the theory

## Slide 9: Drag – Analytical solution
Our theory suggests, that the main sources of drag would be:
Constant drag from the bearing friction – constant in respect to (denoted )
Turbulent drag on the spinner geometry – quadratic in respect to (denoted )
… denotes the total time before the spinner stops
Measurements
 | Drag equation with coefficients
Differential equation | 
Solution | 
Differential equation | 
Solution | 
()

## Slide 10: Drag – Comparison with measurement
Measurements
Spinner decay in time
In a „quasi-homogenous“ magnetic field
No external magnetid field
Angular velocity [rad/s]
Time [s]
Time [s]
Notes: Here we compare how well our simulation handles the linear component
The measurements is exceptionally close to the theory

## Slide 11: Drag – External magnetic field
Additional information
The large magnet is modeled as a single magnetic dipole at its center
Notes: Draw the magnet layout!!

## Slide 12: Moment of inertia
Calculated from the model of a physical pendulum
The spinner was suspended with magnets attached to one arm and left to swing freely
Our result are comparable to results found online:
https://www.wired.com/2017/05/physics-of-a-fidget-spinner/
Additional information
Notes: Moment of inertia = moment setrvačnosti
Angular momentum = moment hybnosti
Torque = moment síly
Physical pendulum = fyzické kyvadlo

## Slide 13: Remanence
Can be either calculated from the generated magnetic field or from the force between the magnets
Simplifying the previous equations for dipole force and magnetic field:
We used both methods:
  The force was measured via a scale (used for a singular magnet)
  The field was measured using a mobile phone magnetometer (with the Earth‘s magnetic field being accounted for)
Additional information

## Slide 14: Remanence - results
We measured for 1, 2 and 3 cube magnet stacks as well as a larger (old) NdFeB magnet
Additional information

## Slide 15: Remanence – more data
Additional information
t [s]
B [T]

## Slide 16: Magnetic coupling
Two spinners (one driven) rotating at roughly the same velocity => coupling
Qualitative notes:
  Gradual changes do not break the coupling; abrupt changes do
  The higher the driving velocity is, the less velocity mismatch is acceptable
  Different modes (velocity ratios) are also possible, though even less forgiving
Observed modes are multiples (2:1, 3:1 …) or integer reciprocals (1:1, 1:2 …) of the driving velocity
Driven spinner exp.
Notes: We observed, that when two spinners (with one being driven by a motor) are rotating at roughly the same velocity, the second spinner becomes coupled and continues keeping the same velocity even during gradual changes

## Slide 17: Magnetic coupling results
Driven spinner exp.
Notes: Oscillation when dropping into a lower mode! We‘ll talk about that later some more

## Slide 18: Magnetic coupling results
Driven spinner exp.

## Slide 19: Simulation - Relevant phenomena
Magnet interactions
  We used cubic NdFeB magnets (5mm, grade N35)
  We modeled each magnet as a magnetic dipole
  Force interaction:
  Torque due to generated magnetic field:
Other forces on the spinner – we were not able to simulate these:
  Concentric forces on the ball bearing => increasing friction
  Oscillations and rattling of the ball bearings
Simulation
Magnetic dipole moment:
Notes: Magnetic dipole approximation breaks down at small distances (comparable to the size of the magnet)

## Slide 20: Simulation - Implementation
Simulation
Takes the initial state as input:
  Positions of spinners, initial angles and angular velocities (only in 2D)
  Each magnet interacts with every other magnet using the magnetic dipole model
  From this we calculate the torques on all the spinners:
  The simulation is further improved using the RK4 method
Notes: Two RK4 passes

## Slide 21: Simulation – Methods
Additional information
Tested RK methods:
Euler method
Midpoint method
Heun‘s method
Ralston‘s method
3/8-rule
RK4
Ralston‘s fourth order
Notes: Two RK4 passes

## Slide 22: Simulation – Methods
Additional information
Single RK4 pass (blue) versus
Double RK4 pass (orange)
Notes: Two RK4 passes

## Slide 23: Simulated coupling
Oscillations around the driving velocity equllibrium were both observed and simulated
The amplitudes/frequencies match somewhat (), but our measuring accuracy isn‘t telling of the microscopic behaviour
The main cause for this mismatch would be the poor quality of spinner ball bearings and inconsistent drag coefficiets between spinners
Simulation

## Slide 24: Chaos categorization
Chaos
Simulating behaviours in respect to parameters:
  Starting velocity ratio
  Distance
Automated categorization using:
  Standard deviation
  Linear fit slope
  Passing through 0

## Slide 25: parameter space
Chaos
The stable interval size tapers off with increasing distance
Critical line between chaos and weak interaction
Increasing mode islands get smaller in size
Non-integer modes are also observed

## Slide 26: parameter space
Chaos

## Slide 27: parameter space
Chaos

## Slide 28: parameter space
Chaos
The stable interval size tapers off with increasing driving velocity
New, previously unobserved, non-integer modes also occured:
3:2, 4:3, 6:5, 2:3
Fractal-like borders around stability island 1:1 are observed

## Slide 29: parameter space
Chaos

## Slide 30: Sub-period behaviour
Our algorithm compares the behaviour of an undisturbed spinner and a driven (disturbed) spinner
The angular displacement of an undisturbed spinner grows linearly in time (constant angular velocity)
We also talk about a „sub-period (denoted )“ which means the time it takes for the spinner to rotate from one arm to the next arm
Measurements were done using a Vernier magnetic field meter
Additional information

## Slide 31: Sub-period behaviour - Angle
Additional information

## Slide 32: Sub-period behaviour - Velocity
Additional information
The extremely high error is due to the algorithm used, which has high uncertainty when the tangent is close to 0
Many other phenomena, like the rattling of the bearing, might be having effect on the real velocity during one sub-period => simulation and measurement doesn‘t match up too well

## Slide 33: Torque transfer - Setup
Driven spinner exp.
The driven spinner has a metal plate added to it to increase air resistance
Measuring the transferred torque from the maximum angular velocity, at which the spinners stay coupled

## Slide 34: Air drag
Torque transfer
The parameter has increased tenfold after adding the resisitive plate
A naive air drag model could also be devised like so:

## Slide 35: Braking torque
Torque transfer
The braking torque grows quadratically in respect to angular velocity
The naive air drag model is not awfully far off, but the coeficient is very debatable, which is why we didn‘t use this in the end
We can use this to get the torque transferred to the coupled spinner

## Slide 36: Braking torque calculation
Additional data

## Slide 37: Torque transfer results
Torque transfer
We measured the transferred torque in respect to: spinner to spinner distance, magnet count

## Slide 38: Power transfer
Torque transfer
Maximum transferred power when and
Notes: (There is no physical background, to support the actual shape of the fit)

## Slide 39: Transfer efficiency
Torque transfer
We measured the transfer efficiency in respect to: spinner to spinner distance, magnet count
The efficiency is very low (<1%) !FIX THIS! !FIX GRAPHS!
Notes: (There is no physical background, to support the actual shape of the fit)

## Slide 40: Torque transfer improvements
Torque transfer
Some of the reasons, why the efficiency is so low:
  In normal magnetic transmissions, alternating pole-pairs are used instead of individual magnets with the same orientation
  The magnetic field lines travel mostly through air, thus decreasing the efficiency
  The torque on the magnetic moments in the vertical orientation is always zero – changing the orientation could improve the efficiency
  The magnets are only repelling each other, but attraction might be helpful in stabilizing the transfer

## Slide 41: Magnetic transmissions
Magnetic transmissions
Changes required to increase torque transfer:
  Magnet distance reduction
  Increased magnetic strength
  Use of pole pairs (PP) magnetic teeth
  Using magnetic teeth, we can create magnetic equivalents of almost all standard mechanical gears
Better than mechanical gear equivalents, however, are more complex gears using a modulator
Notes: Na principu podobném našim spinnerům fungují i magnetické převody, které jsou řádově silnější.
Hlavním rozdílem mezi spinnery a mag. převodovkami je použití pólových párů s opačnými póly vedle sebe.
Tímto se vytvoří takový pomyslný magnetický zub a pomocí toho jsme schopni vytvořit magnetické ekvivalenty všech možných ozubených soukolí.
Lepší jsou však magnetické převody, které používají tzv. modulátor.
--------------------------------------------------------
Šnekový převod
ozubený hřeben s pastorkem
kuželové ozubené kolo
vnější čelní ozubené kolo
vnitřní čelní ozubené kolo
planetové soukolí

## Slide 42: Magnetic transmissions- principle
Magnetic transmissions
An appropriately designed modulator modulates the MFL of the outer rotor in such way, that they match with the inner rotor
Fixed modulator:
Fixed oute rotor:
PP count:
Modulator steel poles:
Notes: Modulátor, jak již z názvu vyplývá, moduluje magnetický tok tak, aby perioda vnějšího rototu odpovídala periodě vnitřního rotoru.
K modulování se používají látky s vysokou permeabilitou a počet modulátorových nástavců musí být roven součtu vnitřních a vnějších pólových párů.
Modulace funguje tak, že každý modulátorový nástavec je posunut o krapet menší úhel, než je úhel mezi vnějšími pólovými páry.
Tím získáváme plynulou vlnu, jejíž perioda je stejná jako perioda vnitřního rotoru.
…

## Slide 43: Our design (2. version)
  Modulator gearbox with ratio 1:3 or 1:4
  3D design: Fusion 360
  Comprised of 5 parts:
    Inner rotor
    Modulator body
    Modulatir cap
    Outer rotor body
    Outer rotor cap
  NdFeB N42 3x4x22mm magnets
  Modulation done via transformer steel plates
Magnetic transmissions
Notes: No a nyní se dostáváme k mému vlastnímu návrhu.
Jedná se o modulátorovou převodovku s převodem 1:3.
Byla navržena v programu Fusion 360 a skládá se z 5 částí.
Vnitřní rotor má 4 PP, vnější 12 PP a tedy 16 modulátorových nástavců.

## Slide 44: Design detail
Magnetické převody
Notes: Zde je detail a řez návrhem.
Vlevo vidíme modulátor s drážkami na vložení nástavců.
Uprostřed je vnější rotor, který v sobě má 24 otvorů pro magnety.
Vpravo je vidět řez modelem.

## Slide 45: Transmission characteristics
Magnetic transmissions
Torque during skip-period at different angular velocities
Maximum torque and recoil in respect to
Torque [Nm]
Period count [arb. u.]
Angular velocity [rad/s]
Torque [Nm]

## Slide 46: Summary
Summary
We successfully observed, sustained and simulated the magnetic coupling of spinners
We determined the transferred torque and power
We have a working simulation, which we‘ve compared with measurements
Using the simulation we deduced fractal-like behaviour in respect to multiple parameter
We analytically modeled the effects of drag and confirmed our model with measurements:
We measured the parameters of our spinners and magnets
We created a functioning magnetic gearbox